Direct I
size 12{H \( z \) = { {N \( z \) } over {D \( z \) } } =K { { Sum cSub { size 8{m=0} } cSup { size 8{M} } {b rSub { size 8{m} } z rSup { size 8{ - m} } } } over {a rSub { size 8{0} } + Sum cSub { size 8{m=1} } cSup { size 8{N} } {a rSub { size 8{m} } z rSup { size 8{ - m} } } } } } {}
Non-canonic Direct I
; (a0=1)
N(z)
Ku[k]
feedback coefficients.
Lesson 18

---
size 12{H \( z \) = { {N \( z \) } over {D \( z \) } } =K { { Sum cSub { size 8{m=0} } cSup { size 8{M} } {b rSub { size 8{m} } z rSup { size 8{ - m} } } } over {a rSub { size 8{0} } + Sum cSub { size 8{m=1} } cSup { size 8{N} } {a rSub { size 8{m} } z rSup { size 8{ - m} } } } } } {}
Canonic Direct II
N(z).
Ku[k]
feedback coefficients.
Traditionally state ordering
N 1
Lesson 18

---
What are their differences?
Alternative Direct II Form.
Lesson 18

---
(Super diagonal)
size 12{A= left ( matrix { 0 {} # 1 {} # 0 {} ## 0 {} # 0 {} # 1 {} ## 0 "." "25" {} # - 0 "." 5 {} # 0 "." 5{} } right );```b= left ( matrix { 0 {} ## 0 {} ## 1 } right );``c= left ( matrix { 0 "." "065" {} ## - 0 "." "815" {} ## 0 "." 0 } right );``""d=1} {}
x3
x2
x1
(Traditional ordering)
Lesson 18

---
Alternative Direct II with MATLAB ordering
x1
x2
x3
State ordering has changed?
Lesson 18

---
Non-canonic
Lesson 18

---
Canonic
Lesson 18

---
Canonic
Lesson 18

---
size 12{c= left [ matrix { - 1 {} ## 2 } right ]} {}
Step 3: State Assignment.
size 12{H \( z \) =1+ { {2z rSup { size 8{ - 1} } - z rSup { size 8{ - 2} } } over {1 - 2z rSup { size 8{ - 1} } +z rSup { size 8{ - 2} } } } } {}
negate
size 12{b= left [ matrix { 0 {} ## 1 } right ]} {}
size 12{A= left [ matrix { 0 {} # 1 {} ## - 1 {} # 2{} } right ]} {}
size 12{d=1} {}

y[k]

-1
2
1
x2[k+1]
x2[k]
x1[k]

T
T
u[k]
x1[k+1]
1
2
-1

Lesson 19

---
size 12{A= left [ matrix { 0 {} # 1 {} ## - 1 {} # 2{} } right ]:``b= left [ matrix { 0 {} ## 1 } right ];``c= left [ matrix { - 1 {} ## 2 } right ];`d=1} {}
Final alternative form with
traditional ordered Direct II.
Check
alignl { stack { size 12{H \( z \) =c rSup { size 8{T} } \( ital "zI" - A \) rSup { size 8{ - 1} } b+d= left [ matrix { - 1 {} # 2{} } right ] left [ matrix { z {} # - 1 {} ## 1 {} # z - 2{} } right ] rSup { size 8{ - 1} } left [ matrix { 0 {} ## 1 } right ]+1} {} # `````````= left [ matrix { - 1 {} # 2{} } right ] { { left [ matrix { z - 2 {} # 1 {} ## - 1 {} # z{} } right ]} over {z rSup { size 8{2} } - 2z+1} } left [ matrix { 0 {} ## 1 } right ]+1= { {2z - 1} over {z rSup { size 8{2} } - 2z+1} } +1= { {z rSup { size 8{2} } } over {z rSup { size 8{2} } - 2z+1} } {} } } {}

Lesson 19

---
Direct II – traditional order
size 12{H \( z \) = { {N \( z \) } over {D \( z \) } } = { { Sum cSub { size 8{m=0} } cSup { size 8{M} } {b rSub { size 8{m} } z rSup { size 8{ - m} } } } over {1+ Sum cSub { size 8{m=1} } cSup { size 8{N} } {a rSub { size 8{m} } z rSup { size 8{ - m} } } } } } {}
Lesson 19

---
Direct II alternative form with traditional ordering.
size 12{H \( z \) =b rSub { size 8{0} } + { { \( b rSub { size 8{1} } - b rSub { size 8{0} } a rSub { size 8{1} } /a rSub { size 8{0} } \) z rSup { size 8{ - 1} } + "." "." "." + \( b rSub { size 8{N} } - b rSub { size 8{0} } a rSub { size 8{N} } /a rSub { size 8{0} } \) z rSup { size 8{ - N} } } over {1+a rSub { size 8{1} } z rSup { size 8{ - 1} } + "." "." "." +a rSub { size 8{N} } z rSup { size 8{ - N} } } } =d rSub { size 8{0} } +```` left ( { { Sum cSub { size 8{m=0} } cSup { size 8{M} } {c rSub { size 8{m} } z rSup { size 8{ - m} } } } over {1+ Sum cSub { size 8{m=0} } cSup { size 8{M} } {a rSub { size 8{m} } z rSup { size 8{ - m} } } } } right ) "." } {}
Lesson 19

---
The cascaded transfer functions of the 3rd order filter are given by:
2 cascaded Direct II sections of order 1 and 2.
How do I build this filter?
size 12{H \( z \) = ital "GH" rSub { size 8{1} } left (z right )H rSub { size 8{2} } left (z right )= { {1 - 0 "." "8813"z rSup { size 8{-1} } } over {1 - 0 "." 5z rSup { size 8{-1} } } } times { {1+0 "." "3813"z rSup { size 8{-1} } +0 "." "021"z rSup { size 8{-2} } } over {1+0 "." 5z rSup { size 8{-2} } } } } {}
Lesson 19

---
y[k]


H1(z)
H2(z)
0.3813
-0.479
x1[k]
x2[k]
x3[k]



T
-0.8813
T
T
u[k]
-0.5
0.5
Lesson 19

---
Parallel
size 12{H left (z right )=β rSub { size 8{0} } + Sum cSub { size 8{i=0} } cSup { size 8{Q} } { { {β rSub { size 8{0k} } +β rSub { size 8{1k} } `z rSup { size 8{ - 1} } } over {α rSub { size 8{0k} } +α rSub { size 8{1k} } `z rSup { size 8{ - 1} } +α rSub { size 8{2k} } `z rSup { size 8{ - 1} } } } } } {}
Of less importance, the parallel form
Lesson 19

---
Transposed Architecture
Re-engineer a given architecture
Reverse the direction of flow in all branches.
Reverse the input and output ports.
All nodes become summers, and all summers become nodes.
Result is called a transposed architecture.
Lesson 17

---
Direct
size 12{H left (z right )= Sum cSub { size 8{ ital "k="0} } cSup { size 8{ ital "N-"1} } {h rSub { size 8{k} } } z rSup { size 8{ - k} } } {}
Direct impulse response?
Lesson 20

---
Direct Transpose
size 12{H left (z right )= Sum cSub { size 8{ ital "k="0} } cSup { size 8{ ital "N-"1} } {h rSub { size 8{k} } } z rSup { size 8{ - k} } } {}
Impulse response?
Lesson 20